## Slide 1: Image Processing INT3404 20
Lecturer: Nguyen Thi Ngoc Diep, Ph.D.
Email: ngocdiep@vnu.edu.vn
Notes: 7 13h00’  13h50’ 10’
8 14h00’  14h50’ 10’
9 15h00’  15h50’

## Slide 2: Schedule
Week | Content | Homework
1 | Introduction | Set up environments: Python 3, OpenCV 3, Numpy, Jupyter Notebook
2 | Digital image – Point operations Contrast adjust – Combining images | HW1: adjust gamma to find the best contrast
3 | Histogram - Histogram equalization – Histogram-based image classification | Self-study
4 | Spatial filtering - Template matching | Self-study
5 | Feature extraction Edge, Line, and Texture | Self-study
6 | Morphological operations | HW2: Barcode detection  Require submission as mid-term test
7 | Filtering in the Frequency domain Announcement of Final project topics | Final project registration
8 | Color image processing | HW3: Conversion between color spaces, color image segmentation
9 | Geometric transformations | Self-study
10 | Noise and restoration | Self-study
11 | Compression | Self-study
12 | Final project presentation | Self-study
13 | Final project presentation Class summarization | Self-study

## Slide 3: Schedule
Tuần | Nội dung | Yêu cầu đối với sinh viên (ngoài việc đọc tài liệu tham khảo)
1 | Giới thiệu môn học | Cài đặt môi trường: Python 3, OpenCV 3, Numpy, Jupyter Notebook
2 | Ảnh số (Digital image) – Phép toán điểm (Point operations) Làm quen với OpenCV + Python Điều chỉnh độ tương phản (Contrast adjust)– Ghép ảnh (Combining images) | 
3 | Histogram - Histogram equalization | Làm bài tập 1: điều chỉnh gamma tìm contrast hợp lý
4 | Phép lọc trong không gian điểm ảnh (linear processing filtering) | Thực hành ở nhà
5 | Phép lọc trong không gian điểm ảnh (linear processing filtering) (cont.) Thực hành: Cách tìm filters | Thực hành ở nhà
6 | Thực hành: Ứng dụng của histogram; Tìm ảnh mẫu (Template matching) | Bài tập mid-term
7 | Trích rút đặc trưng của ảnh Cạnh (Edge) và đường (Line) và texture | Thực hành ở nhà
8 | Các phép biến đổi hình thái (Morphological operations) | Làm bài tập 2: tìm barcode
9 | Chuyển đổi không gian – Miền tần số – Phép lọc trên miền tần số Thông báo liên quan đồ án môn học | Đăng ký thực hiện đồ án môn học
10 | Xử lý ảnh màu (Color digital image) | Làm bài tập 3: Chuyển đổi mô hình màu và thực hiện phân vùng
11 | Các phép biến đổi hình học (Geometric transformations) | Thực hành ở nhà
12 | Nhiễu – Mô hình nhiễu – Khôi phục ảnh (Noise and restoration) | Thực hành ở nhà
13 | Nén ảnh (Compression) | Thực hành ở nhà
14 | Hướng dẫn thực hiện đồ án môn học | Trình bày đồ án môn học
15 | Hướng dẫn thực hiện đồ án môn học Tổng kết cuối kỳ | Trình bày đồ án môn học

## Slide 4: Recall week 2: Digital image

## Slide 5: Recall week 2: Quantization levels
Conventional grayscale image has 256 levels
Image credit: Bernd Girod

## Slide 6: Recall week 2: Point operations
Aka: Point-processing transformations
  Image pixel intensities are transformed into a different set of intensities based on input-output mappings
Gamma transformation
  Concept of “Lookup table (LUT) based mapping”
Thresholding
Arithmetic operations
Set and logical operations

## Slide 7: Week 3
Histograms

## Slide 8: Why study histogram processing?
Histogram manipulation is a fundamental tool in image processing
Histograms:
  Simple to compute
  Suitable for fast hardware implementations
  Popular tool for real-time image processing
Histogram shape is related to image appearance

## Slide 9: Histogram
An image with L-level intensities
: intensity level k (k = 0, 1, 2, ... , L-1)
: number of pixels with intensity
Unnormalized histogram:
Normalized histogram:
M: height of image = number of image rows
N: width of image = number of image columns
The subdivisions of the intensity scale are called histogram bins
0
256
1
Normalized histogram:

## Slide 10: Histogram shape and image appearance
Notes: Histogram bins are concentrated on the lower (dark) end of intensity scale
The most populated bins are biased toward the higher end of the scale
Low-contrast (dull image)  narrow histogram located typically toward the middle of the intensity scale
High-contrast image  cover a wide range of the intensity scale

## Slide 11: Color image

## Slide 12: Histogram equalization
(Cân bằng biểu đồ mức xám)
A special contrast enhancement technique

## Slide 13: Histogram equalization
How?
Objective: To improve the dynamic range and contrast of an image
Reassigning pixel intensity values such that the resulting image has a (close to) uniform distribution across its entire range of values
Meaning, having a flat intensity histogram

## Slide 14: Image integrity
Intensity reassignments must preserve image integrity
  Not affect the intensity information structure (intensity ranking) with respect to the pixel geometry
bright   dark

## Slide 15: ”Pixel geometry”
Map/
Transform
Pixel lookup table
Preserving the image structure by:

## Slide 16: Histogram equalization algorithm
Or
Step 1: 0 -> 4
Sum(rk=0) = sum(sk->4)
If not sum not equal
0  3
Rk=1
Sk=3
N pixels
L muc xam
N/L

## Slide 17: Cumulative Intensity Histogram
C_r(k) = C_s(k)

## Slide 18: Note
All image pixels with the same intensity in the original image cannot be assigned to different intensities but be mapped to the same new value all together.
 Perfect histogram equalization will not be possible for digital images due to discrete values

## Slide 19: Characteristics of histogram equalization
Monotonically increasing function

## Slide 20: Steps of Histogram equalization
Compute the intensity histogram and/or cumulative intensity histogram of the original image
Compute the lookup table
Transform the original image using the lookup table

## Slide 21: HE example
Source: Gonzalez et al.

## Slide 23: Implementation
Refer to source code

## Slide 24: Local histogram equalization

## Slide 25: Local histogram processing
Global histogram processing: a transformation function modifies the intensity distribution of an entire image
  Suitable for overall enhancement
Local histogram processing: modifies intensity distribution of pixel neighborhoods
  To enhance details over small areas in an image
  Two approaches:
    Non-overlapping regions  can produce an undesirable “blocky” effect
    Overlapping  more computation

## Slide 26: Example of local histogram equalization
Using a neighborhood of size 3x3

## Slide 27: Contrast Limited Adaptive Histogram Equalization (CLAHE)
Image is divided into small blocks called "tiles" (e.g., 8x8 pixels).
Each block is histogram equalized as usual.
In a small area, histogram would confine to a small region (unless there is noise).
If noise is there, it will be amplified --> to avoid this, *contrast limiting is applied.
If any histogram bin is above the specified contrast limit (e.g., 40), those pixels are clipped and distributed uniformly to other bins before applying histogram equalization. After equalization, to remove artifacts in tile borders, bilinear interpolation is applied.
Ref: - Campos, Gabriel Fillipe Centini, et al. "Machine learning hyperparameter selection for Contrast Limited Adaptive Histogram Equalization." EURASIP Journal on Image and Video Processing 2019.1 (2019): 59.
- https://docs.opencv.org/master/d2/d74/tutorial_js_histogram_equalization.html

## Slide 28: Histogram matching
As known as “Histogram Specification”

## Slide 29: Histogram matching
source
template
Histogram Matching
A transformation function that generates an output image with a specified histogram
Histogram Equalization
A transformation function that generates an output image with a uniform histogram

## Slide 30: Histogram matching
z
source
template
T(r)
G(z)
Histogram equalization
Histogram equalization

## Slide 31: Steps of histogram matching
Compute the histogram of the input image and do the histogram equalization from rk to sk
Compute histogram of the template image and do the histogram equalization from zq to s’q
For each sk, find zq such that G(zq) is close to sk
Do the transformation
r  sk  zq

## Slide 32: Histogram matching example
z
G
G-1

## Slide 33: Image retrieval using histogram

## Slide 34: Giới thiệu bài toán
Tìm ảnh trong tập dữ liệu ảnh gần giống với ảnh đầu vào nhất
Dataset
Input
 Bài toán sắp xếp

## Slide 35
Computation space
Sorting
Retrieval/search
Clustering
classification
fun

## Slide 36: Image retrieval algorithm
For each image in the dataset D
  Calculate the channel-wise histogram
  Stack histograms to make 1D vector (as feature vector)
Given an input image, do step 1 to obtain the feature vector (q)
Do vector similarity calculation between vector q and vectors in D
Return the corresponding images which have the most similar feature vectors to q

## Slide 37: Implementation
Refer to source code